## Slide 1
ximg
yimg
xser
Standard Readout
Electron-Multiplying Readout
Parallel Pixel
Serial Pixel
Serial Over-Scan
Additional Serial Pixels (Corner, etc)
Pixel.m
Detector.m
Controller.m
Charge Measurement
Charge Transfer
Charge Generation
Image Processing
Charge Collection
Electron-Multiplying Pixel

## Slide 2: Initial Testing
Performing initial testing of CCD_Sim to check out basic functionality / verify expected behavior / performance
Simulated 1000 read-outs with 0.01 s integration time
Test image used shown below
  Red pixels have 10 photons s-1 mean incidence rate
  White pixels have 1 photons s-1 mean incidence rate
Detector Property | Value
Parallel Section Width | 12 Pixels
Parallel Section Length | 12 Pixels
Serial Overscan | 2 Pixels
Additional Serial Pixels | 2 Pixels
Multiplication Elements | 50 Pixels
Read Out Noise (RMS) | 3 e-
Vertical Frequency | 0.9e6 Hz
Horizontal Frequency | 1e6 Hz
Pixel Property | Value
CTE | 0.999999
Dark Current Rate | 0.0015 e- s-1
Pixel Length | 13 μm
Pixel Width | 13 μm
Parallel Pixel Property | Value
Interacting Quantum Efficiency | 0.9
Quantum Yield | 1.2
Full Well Capacity | 80k e-
CIC Rate | 1e-4 e- tr-1
Serial Pixel Property | Value
Full Well Capacity | 360k e-
CIC Rate | 1e-3 e- tr-1
EM Multiplication Probability | 0.1
Test Image
As Entered

## Slide 3
Initial Testing
Results shown are for standard (non-photon-counted) output, coadding the 1000 read-outs to arrive at a final image

## Slide 4
Results shown are for photon-counting of previous data, using 5-sigma threshold above the read-noise
Initial Testing

## Slide 5
Results shown are with electron multiplication disabled (read out through the standard register)
Initial Testing

## Slide 6
Initial Testing
Results shown are for standard (non-photon-counted) output, coadding the 1000 read-outs to arrive at a final image
CTE has been set to 0.99 for all pixels

## Slide 7
Results shown are for photon-counting of previous data, using 5-sigma threshold above the read-noise
CTE has been set to 0.99 for all pixels
Initial Testing

## Slide 8
\delta E is the FWHM energy of the observed spread in electrons, E in eV